## Slide 1: Engineering the LPG PUV Using an OEM Vehicle Platform
UP NCTS – DOST – DOE Project

## Slide 2: Original Project Objectives
a) Use an OEM vehicle platform, light truck or pick up (cab and chassis), to develop a jeepney design of 18-20 passengers that conform to PNS 2111:2015 CLRV Dimensional Limits
b) Introduce weight reduction measures in the body design
c) Construction using OEM-approved manufacturing processes a prototype of this jeepney design
d) Road-test the prototype jeepney design

## Slide 3: Project Objectives vs. Accomplishments
a) Use an OEM vehicle platform, light truck or pick up (cab and chassis), to develop a jeepney design of 18-20 passengers that conform to PNS 2111:2015 CLRV Dimensional Limits
Final prototype was constructed using an OEM vehicle platform with 18-passenger capacity conforming with PNS 2126:2017, PUV Class I (9-22 passengers, all seated); UNECE Category M2 Class B

## Slide 4: Project Objectives vs. Accomplishments
Introduce weight reduction measures in the body design
Final prototype was constructed with marine plywood and vinyl matting flooring, aluminum window frames, molded fiberglass front and rear body panels

## Slide 5: Project Objectives vs. Accomplishments
Construction using OEM-approved manufacturing processes a prototype of this jeepney design
Final prototype was constructed using a light truck cab and chassis platform and a 2.4-liter brand new gasoline engine retrofitted for LPG fuel
2TZ gasoline engine
Clean Fuel Tartarini LPG system
Naveco X101-28

## Slide 6
Road-test the prototype jeepney design
Final prototype was road tested along a selected UP-Ikot route.
Project Objectives vs. Accomplishments

## Slide 7
d) Road-test the prototype jeepney design
UP-Ikot Road Test Results are shown below.
Project Objectives vs. Accomplishments
* Aircon duty cycle during tests is unknown
Re-tuning (2nd) was performed after the first (1st) tuning LPG test run
Fuel economy difference between LPG and Gasoline is within range of percent difference in Heating Value/liter

## Slide 8
d) Road-test the prototype jeepney design
UP-Ikot Road Test Results are shown below.
Project Objectives vs. Accomplishments

## Slide 9: PHASE 1 Route (SHORT roundtrip length of 13.25 km) Consists of urban driving segments (mostly 2-4 lanes per direction) characterized by stop-and-go conditions because of traffic signals and relatively shorter distances between stops
EASTBOUND Route (SM North to UP Vinzon’s Hall : 6.75 km)

## Slide 10: Overall Accomplishments ( Technical Details )
1. An 18-passenger Auto-LPG PUV built on an OEM vehicle platform compliant with PNS 2126:2017, PUV Class I ; Actually a bi-fuel PUV, runs on either LPG or gasoline.
LPG and Gasoline filling ports

## Slide 11: Overall Accomplishments ( Technical Details )
1. An 18-passenger Auto-LPG PUV built on an OEM vehicle platform compliant with PNS 2126:2017, PUV Class I ; Actually a bi-fuel PUV, runs on either LPG or gasoline.
Body dimensions: LxWxH, stepboard ground clearance, side and emergency doors, wheelbase, front & rear overhangs

## Slide 12: Overall Accomplishments ( Technical Details )
1. An 18-passenger Auto-LPG PUV built on an OEM vehicle platform compliant with PNS 2126:2017, PUV Class I ; Actually a bi-fuel PUV, runs on either LPG or gasoline.
Seated and standing clearances
Seat and partition dimensions
Step board ground clearance

## Slide 13: Overall Accomplishments ( Technical Details )
2. Vertically sliding window panes allowing full window opening to maximize natural ventilation and emergency exit area if necessary
Raising to fully closed, lowered to fully open window positions
Fully closed and partially open windows as seen from the outside

## Slide 14: Overall Accomplishments ( Technical Details )
3. Partitions for long passenger seat to arrest passenger compression during sudden or hard breaking
Seat partitions to arrest passenger compression

## Slide 15: Overall Accomplishments ( Technical Details )
4. Marked seats for PWDs

## Slide 16: Overall Accomplishments ( Technical Details )
5. Digital Signage for Route/Travel info for passengers & PWDs

## Slide 17: Overall Accomplishments ( Technical Details )
6. Public address system for Route/Travel info for passengers & PWDs
Microphone
Front & rear speakers

## Slide 18: Overall Accomplishments ( Technical Details )
7. Electronic fare payment system

## Slide 19: Overall Accomplishments ( Technical Details )
8. CCTV system for security and safety
Pics showing CCTV cameras and monitor displays

## Slide 20: Overall Accomplishments ( Technical Details )
9. Distributed and easy access PUV Stop buttons

## Slide 21: Overall Accomplishments ( Technical Details )
10. Wheelchair Lift System

## Slide 22: Overall Accomplishments ( Technical Details )
Anti-Covid integrated design of AC air flow and distribution using CFD to minimize cross-flow of airborne particles among passengers;
 Separate AC air return/exhaust system designed and installed
Adjusting AC air inlet opening and orientation to conform with CFD analysis
AC air return/exhaust pvc pipes under seats

## Slide 23: Assumptions used for the CFD study
Full cabin capacity (1 driver + 18 passengers)
Volume flow follows the 12 air changes per hour requirement
Modified return ports for the air conditioning system with 5 ports per side of the vehicle (total of 10) under the seats of the passengers
Equal flow coming out of all inlet ports above the cabin occupants at 45° relative to the horizontal
Equal flow going into each return port.

## Slide 24: With rear left exhaust fan NO Return/Exhaust Pipe
Driver Side Airflow (12 Air Changes/Hr)

## Slide 25: With rear right exhaust fan NO Return/Exhaust Pipe
Door Side Airflow (12 Air Changes/Hr)

## Slide 26: Return/exhaust pipes installed under seats
Driver Seat

## Slide 27: Driver Side Airflow (12 Air Changes/Hr)
With rear left exhaust fan WITH Return/Exhaust Pipe

## Slide 28: With rear right exhaust fan WITH Return/Exhaust Pipe
Door Side Airflow (12 Air Changes/Hr)

## Slide 29: Overall Accomplishments ( Technical Details )
Anti-Covid integrated design of AC air flow and distribution using CFD to minimize cross-flow of airborne particles among passengers;
 Separate AC air return/exhaust system designed and installed
Adjusting AC air inlet opening and orientation to conform with CFD analysis
AC air return/exhaust pvc pipes under seats

## Slide 30: 6Ps
1. PUBLICATION
A technical paper is currently being written for publication; waiting for results of UP-Ikot road tests.
PATENTS
We will identify what can be patentable and then file for the appropriate patent.
3. PRODUCTS
A prototype PUV with 18-passenger capacity running on LPG or gasoline is built using an OEM vehicle platform
The PUV is PWD-Friendly, incorporates a wheelchair lift and marked seats
Has visual and audio announcement systems for the hearing- or visually-impaired

## Slide 31: 6Ps
4. PEOPLE SERVICES
N.A.
5. POLICIES
Project Report will give recommendations on the technology approach for pursuing the use of LPG for PUVs.
6. PLACES & PARTNERSHIPS
N.A.

## Slide 32: Plans after project completion
Help push for the use of LPG in PUVs as a transition measure while waiting for EV use to be feasible for mainstream public transport
  Propose for actual deployment of LPG PUV prototype or similar units in the SM North – UP route to obtain both O&M technical and economic data
  Identify/examine the appropriate business model to mainstream LPG use in public transport
Continue CFD analysis with experimental / actual verification of AC and ventilation systems of existing PUVs for immediate application to minimize Covid transmission.

## Slide 33: Thank You

## Slide 35
d) Road-test the prototype jeepney design
UP-Ikot Road Test Results are shown below.
Project Objectives vs. Accomplishments

## Slide 36: PHASE 1 Route (SHORT roundtrip length of 13.25 km) Consists of urban driving segments (mostly 2-4 lanes per direction) characterized by stop-and-go conditions because of traffic signals and relatively shorter distances between stops
EASTBOUND Route (SM North to UP Vinzon’s Hall : 6.75 km)

## Slide 37: PHASE 1 Route (SHORT roundtrip length of 13.25 km)
WESTBOUND Route (UP Vinzon’s Hall to SM North: 6.5 km)

## Slide 38: Table 1 – Summary Data of Phase 1 Test Jeepneys
JEEPNEY | Pass. | Curb Wt. | Engine | Size | Power* | Torque*
 | # | (kg) | (Model) | (ltr.) | (kW @ rpm) | (Nm @ rpm)
2nd Diesel | 20 | 1,200 | Isuzu 4BC2 | 3.3 | 65 @ 3500 | 200 @ 2200
2nd LPG | 20 | 1,500 | Hyundai Theta | 2.0 | 107 @ 6000 | 190 @ 4000
3rd LPG | 22 | 2,280 | Toyota 4RB2 | 2.4 | 106 @ 5000 | 217 @ 4000
2nd Diesel Jeepney
2nd LPG Jeepney
3rd LPG Jeepney
GVW with 22+1 pax:
3,430 kg

## Slide 39: Fuel Economy – On-Road
a – 2nd LPG jeepney ave. Load Factor = 59.81 %
b – 3rd LPG jeepney simulated on-road tests ave. Load Factor = 100 %
2nd LPG Jeepney
3rd LPG Jeepney
GVW with 22+1 pax:
3,430 kg

## Slide 40: Fuel Economy - Laboratory
a – 2nd LPG jeepney
b – 3rd LPG jeepney
2nd LPG Jeepney
3rd LPG Jeepney
GVW with 22+1 pax:
3,430 kg